## Slide 1: Edge AI-Powered Acoustic Surveillance System for Forest Protection
[Student Name 1]
ID: [Student ID]
And
[Student Name 2]
ID: [Student ID]
Department of CSE
Daffodil International University

## Slide 2: Outline
Introduction
Background Study/Literature Review
Gap Analysis
Objective and Motivation
Novelty of this Study
Datasets, Tools and Techniques
Proposed Methodology
Expected Outcomes
Q & A

## Slide 3: Introduction
Forests cover 4.06 billion hectares (31% of Earth's land area), supporting 90% of terrestrial biodiversity
Global forest loss: 10-25 million hectares/year; dominant driver is illegal logging
Traditional monitoring relies on expensive, time-consuming manual ground patrolling
Tree cutting, chainsaws, gunshots produce distinct acoustic signatures detectable by sensors
Proposed: Edge AI acoustic surveillance system using TinyML on ESP32-S3 microcontroller
System classifies 20 forest sound events in real-time with 9.5 ms inference latency
Solar-powered autonomous operation with dual LoRa + GSM communication for alert delivery
Target: Automated, low-cost, 24/7 forest protection in remote environments

## Slide 4: Background Study/Literature Review
Reviewed 33 peer-reviewed papers (2011-2026) from IEEE, Springer, MDPI, ACM
Edge AI/TinyML Systems:
- Singh et al. (2024): STHT + SVM on 32-bit MCU, 96.61% acc, 5 classes
- Ayankoso et al. (2024): CNN+LSTM TinyML on RPi Pico, 89.14%, 3 classes
Deep Learning Approaches:
- Mohmmad et al. (2026): TCN+Transformer, 97.48% but requires GPU, 4 classes
- ForNet (2026): CNN+XGBoost ensemble, 91.4%, 5 classes, server-based
IoT & Communication:
- TreeSpirit (2017): Three-tier WSN + Neural Network
- Andreadis et al. (2021): Ultra-low-power LoRaWAN, months of operation
Key Finding: All systems limited to 2-5 classes; no true edge AI with comprehensive taxonomy

## Slide 5: Gap Analysis
Gap 1: Limited Sound Taxonomy - All systems classify only 2-5 classes
Real forests have 15+ distinct threat types (chainsaws, guns, vehicles, drones...)
Gap 2: No True Edge AI - High-accuracy models (97%) need GPU/server hardware
Edge systems handle only 3 classes with limited accuracy
Gap 3: No Solar Sustainability - Best battery life: 10 hours (Ayankoso 2024)
No complete solar energy budget for perpetual autonomous operation
Gap 4: Single Communication - Systems use LoRa OR GSM, never both adaptively
Gap 5: Analog Microphones - Prone to electrical noise; digital I2S underutilized
Gap 6: No PCEN - Per-Channel Energy Normalization never applied to forest acoustics

## Slide 6: Objective and Motivation
Objectives:
1. Design 20-class acoustic classifier using SE-DS-CNN (27.4 KB INT8) on ESP32-S3
2. Achieve sub-10 ms inference for real-time continuous monitoring
3. Develop solar-sustained node (1.6 hrs sunlight/day for perpetual operation)
4. Implement dual-mode LoRa + GSM with MOSFET power switching
5. First application of PCEN for forest acoustic surveillance
6. Comprehensive evaluation across 20-class taxonomy (largest in literature)
Motivation:
- 25 million hectares of forest lost annually due to illegal logging
- Manual patrolling is expensive and cannot cover vast forest areas 24/7
- Existing tech solutions are too limited (2-5 classes, server-dependent, short battery)
- Need: autonomous, intelligent, edge-deployed monitoring for remote forests

## Slide 7: Novelty of this Study
1. Most Comprehensive Sound Taxonomy
20 classes vs. max 5 in literature (4x more comprehensive)
2. Smallest Edge-Deployed Model
27.4 KB INT8 with 9.5 ms inference - smallest and fastest on MCU
3. First PCEN for Forest Acoustics
Automatic noise-floor adaptation for variable outdoor environments
4. Best Power Sustainability
5.4 days battery autonomy; 1.6 hrs sunlight for perpetual operation (13x better)
5. Only Dual-Mode Communication
Adaptive LoRa + GSM with MOSFET hardware power gating

## Slide 8: Datasets, Tools and Techniques
Dataset: 5,200 audio clips | 20 classes | 16 kHz, 16-bit mono | 2-sec windows
Sources: ESC-50, UrbanSound8K, Rainforest Connection (RFCx), Google AudioSet
Split: 70% Train / 15% Validation / 15% Test (stratified)
Sound Classes: Forest ambient, Chainsaw, Axe, Handsaw, Gunshot, Explosive,
Heavy Machinery, Vehicle, Motorcycle, Drone, Speech, Shouting, Footsteps,
Footsteps-leaves, Digging, Tree Falling, Campfire, Hunting Dog, Walkie-talkie
Hardware: ESP32-S3, INMP441 I2S mic, RFM95W LoRa, SIM800L GSM, Neo-6M GPS
Software: Python, TensorFlow/Keras, TF Lite Micro, Edge Impulse, Arduino IDE
Librosa, NumPy, Scikit-learn, Matplotlib
Techniques: PCEN/MFE/Log-Mel features, SE-DS-CNN, INT8 quantization, 5-fold CV

## Slide 9: Proposed Methodology
Audio Pipeline: INMP441 Mic -> Pre-process -> PCEN/MFE Features -> SE-DS-CNN -> Alert
Model: SE-DS-CNN (Squeeze-and-Excitation Depthwise-Separable CNN)
- Depthwise-Separable Conv: 8-9x fewer computations vs standard CNN
- SE Block: channel attention for frequency band weighting (+3-5% accuracy)
- INT8 Quantization: 4x compression (110 KB -> 27.4 KB), <1% accuracy loss
Duty Cycle Operation:
Deep Sleep (8s, 15uA) -> Wake & Sample (2s, 100mA) -> Inference (9.5ms)
-> Alert if threat (LoRa 20mA / GSM 350mA, 15s) -> Return to Sleep
Communication: LoRa primary (low power) -> GSM fallback (if no gateway)
MOSFET power switch physically disconnects GSM when not needed (0mA standby)
Power: LiFePO4 battery + 3-panel solar array | 5.4 days without solar

## Slide 10: Expected Outcomes
Preliminary Results (Phase 1):
Overall Accuracy: 88.21% | Precision: 91.26% | F1-Score: 89.84%
11/20 classes achieved perfect F1 = 1.00 (axe, explosive, machinery, speech...)
Model: 27.4 KB | Inference: 9.5 ms | Deep Sleep: 15-20 uA
Expected Final Outcomes:
1. Field-deployed 20-class acoustic surveillance system in real forest
2. Improved accuracy for challenging classes (chainsaw 82% -> 90%+)
3. Validated solar sustainability with >30 days continuous autonomous operation
4. Cloud dashboard for real-time alert visualization and monitoring
5. Mobile app for forest officers to receive threat notifications
Comparison: Our system is 4x more classes, 13x better battery, smallest model
vs. all 33 papers reviewed in the literature

## Slide 11
THANK YOU